## Slide 1
Four-Lane Pipelined Shared-Weight FFN
Architectural breakdown for a sequence-parallel Pre-Add-DyT + FFN + Post-DyT transformer block
D = 4096 | HIDDEN_DIM = 11008 | M = 32 LANES = 4 | NUM_COLS = 16 per lane | N = parameterized
Lane 0
1×d vector path
Lane 1
1×d vector path
Lane 2
1×d vector path
Lane 3
1×d vector path
Shared weight-tile cache + ordered output
01

## Slide 2
Design objectives and target configuration
The architecture scales sequence throughput without replicating full N×d storage
2
Process four independent 1×d vectors concurrently.
Keep the per-lane tile size at M=32 and use NUM_COLS=16 per projection.
Reuse one shared weight tile across lanes instead of issuing four independent external reads.
Preserve fixed-point Q8.8 datapaths and the DyT tanh-LUT implementation.
Stream rows in seq_idx order even when lanes complete at different times.
Keep the original single-lane top-level available for regression and comparison.
D
4096
HIDDEN_DIM
11008
M
32
LANES
4
NUM_COLS
16/lane
N
parameterized
Nominal DSP structure: 4 × (2 × 32 × 16 + 4) = 4,112 DSP operators

## Slide 3
Baseline: sequential three-phase architecture
One input vector occupies the datapath until the complete transaction finishes
3
Input 1×d
Pre-Add-DyT
FFN Fetch → Up → ReLU → Down → Acc
Post-Add-DyT
Output 1×d
One phase active at a time.
No lane scheduler or output reorder.
Weight reads originate from the active lane fetch FSM.
Simple control and verification.
Latency grows linearly with sequence length N.
Hardware resources are underutilized for batched vectors.

## Slide 4
New top-level: four concurrent sequence lanes
The scheduler dispatches row indices; lanes share weights but retain private activation state
4
Sequence Scheduler
Lane 0
seq_idx 0
Lane 1
seq_idx 1
Lane 2
seq_idx 2
Lane 3
seq_idx 3
Shared weight-tile cache / AXI arbiter
External memory AXI read channel
Output reorder by out_seq_idx
Ordered N×d output stream
Key principle: the sequence dimension is parallelized; the model weights remain common.

## Slide 5
Inside each lane
Each lane retains the verified three-phase datapath and owns its active-vector buffers
5
Pre-Add-DyT
x + residual α·z → tanh → γ·tanh+β
Local BRAM
norm_input / residual
FFN Fetch
tile addresses input + ReLU BRAM
Up Projection
M×NUM_COLS multipliers
ReLU
Q8.8 max(0,x)
Down + Acc
projection + saturation
Post-Add-DyT
FFN output + residual
Tile size: M=32.
Projection parallelism: NUM_COLS=16.
DyT: two DSP multipliers per phase.
Tanh: 1024-entry BRAM LUT.
Accumulator uses widened signed arithmetic and Q-format-aware extraction.
Lane runs in SINGLE_VECTOR mode for one dispatched seq_idx.

## Slide 6
Sequence scheduler and lane groups
N vectors are dispatched in groups of four, with masking for the final partial group
6
Example dispatch for N=10
Group 0
Lane 0 seq 0
Lane 1 seq 1
Lane 2 seq 2
Lane 3 seq 3
Group 1
Lane 0 seq 4
Lane 1 seq 5
Lane 2 seq 6
Lane 3 seq 7
Group 2
Lane 0 seq 8
Lane 1 seq 9
Lane 2 seq —
Lane 3 seq —
IDLE
DISPATCH
RUN
STREAM
DONE
The scheduler does not replicate N full datapaths; it reuses four lanes and tracks row identity explicitly.

## Slide 7
Shared weight-tile cache and broadcast methodology
One common weight region is accessed through a shared AXI/cache path
7
Lane requests weight tile
Tile request coalescer
M×M tile cache/replay
AXI DMA
Lane 0
Lane 1
Lane 2
Lane 3
Tile-level intent • Fetch one complete M×M weight tile. • Keep it in the shared cache. • Replay the same tile to lanes requesting the same address. • Avoid four independent external weight bursts. • Preserve AXI backpressure and burst ordering.
Implementation note: the current wrapper uses a shared cache/replay layer around the existing lane AXI protocol; a native weight_tile_req/weight_tile_valid interface is the next refinement.

## Slide 8
Per-lane buffering and ordered output
Private activation state avoids replicating the full N×d tensor on-chip
8
Lane 0 buffers
norm_input
residual
ReLU
FFN output
Lane 1 buffers
norm_input
residual
ReLU
FFN output
Lane 2 buffers
norm_input
residual
ReLU
FFN output
Lane 3 buffers
norm_input
residual
ReLU
FFN output
Output capture + reorder per-lane beat buffers
seq_idx ordered stream
Output protocol
out_seq_idx identifies the vector row.
out_row_last marks the final beat of one 1×d output.
out_last marks the final beat of the complete N×d transaction.
The reorder stage prevents lane completion order from changing external row order.
The final partial group masks unused lanes.

## Slide 9
Fixed-point datapath and DyT implementation
The parallel architecture preserves the validated Q8.8 arithmetic path
9
Q8.8 input / output
α × z Q16.16
tanh LUT BRAM ROM
γ·tanh + β Q8.8
Tanh LUT: 1024 entries with saturated input range.
Two main DSP multipliers per DyT stage.
Signed wide thresholds protect saturation.
Projection products accumulate in widened registers.
Fraction-aware extraction returns Q8.8 data.
Up projection: 32×16 multipliers per lane.
Down projection: 32×16 multipliers per lane.
Four lanes share the same architecture template.
NUM_COLS trades DSP area for cycles.
N changes scheduling/latency, not lane datapath width.

## Slide 10
Resource organization and DSP budget
10
Block | Per lane | 4 lanes
Up projection | 32×16 = 512 DSP | 2,048 DSP
Down projection | 32×16 = 512 DSP | 2,048 DSP
Pre/Post DyT | 4 DSP | 16 DSP
Nominal total | 1,028 DSP | 4,112 DSP
DSP formula
4 × (2 × M × NUM_COLS + DyT multipliers) = 4 × (2 × 32 × 16 + 4) = 4,112
N=2048 does not replicate datapath hardware.
Weights are external/shared; local buffers are per lane.
BRAM usage grows with lane buffering, not full N×d storage.

## Slide 11
Latency model: calculated comparison
Values shown here are cycle-level calculations, not completed large-N RTL simulation results
11
N | Sequential total | Four-lane total | Calculated improvement
640 | 29.588 s | 7.398 s | 4.00×
1,024 | 47.341 s | 11.837 s | 4.00×
1,152 | 53.258 s | 13.317 s | 4.00×
1,536 | 71.011 s | 17.756 s | 4.00×
1,664 | 76.929 s | 19.236 s | 4.00×
2,048 | 94.682 s | 23.674 s | 4.00×
Model assumptions: M=32, D=4096, HIDDEN_DIM=11008, 500 MHz, four sequential lane groups, shared weight delivery without stalls, and one 1,024-beat output serialization segment per vector.

## Slide 12
Verification and implementation status
Separate verified regressions from large-scale runs that still require completion
12
PASS
Original single-lane regression 16/16 output values pass within Q8.8 tolerance
PASS
Four-lane smoke test Sequence ordering, row markers, and final done behavior pass
PENDING
Large d=4096 sweep N=640..2048 full RTL runs require external long-run simulation

## Slide 13
RTL and verification file map
The new top is additive; the original verified top remains available
13
Core RTL
ffn_block_zynq.v
add_dyt_stage.v
add_dyt_post.v
fetch_addr_gen_dyt.v
tm_proj_stage.v
relu_stage.v
accumulator.v
Parallel RTL
ffn_block_zynq_4lane.v
ffn_block_zynq_4lane_tile_bcast.v
axi_shared_weight_cache.v
Infrastructure
axi_read_master.v
bram_dp.v
adder_tree.v
mul_col.v
tanh_lut.v
defines.v
Testbenches
tb_ffn_4lane_smoke.v
tb_ffn_4lane_latency_large.v
tb_ffn_block_zynq.v
tb_ffn_latency.v

## Slide 14
Key takeaways
Sequence parallelism changes the architecture from one occupied datapath to four concurrent 1×d lanes.
Shared weight-tile handling removes unnecessary duplication of common weight traffic.
Per-lane BRAM and an output reorder stage preserve correctness and row ordering.
The HIDDEN_DIM and N parameters make the architecture scalable and controllable from the top level.
The four-lane point is structurally suited to a device with approximately 5,000 DSP slices.
Large latency values must be reported only after complete RTL simulation reaches out_last and done.
14