## Slide 1
MODIFIED PIPELINED FFN DESIGN
JULY 16, 2026
Different modules, their interconnections in top module, testbench and results

## Slide 2
TABLE OF CONTENTS
01
Introduction
05
Second submodule : axi read master
02
RTL Schematic
06
Third submodule : wide-word bram
03
Synthesized design
07
Stage 1 : Fetch and address generation
04
First submodule : Adder Tree
08
Fetch and address generation FSM

## Slide 3
TABLE OF CONTENTS
09
Stage 2 & 4 : up and down projection
13
Timing diagram
10
Stage 3 : relu
14
Resource utilization
11
Stage 5 : accumulation
12
Testbench output

## Slide 4
INTRODUCTION
Truely Pipelined Feed Forward Network
Features :
5 pipelined stages
Tile-based computation
AXI4 external memory access

## Slide 5
RTL SCHEMATIC
ACCUMULATOR
RELU
DOWN PROJECTION
RELU BRAM
UP PROJECTION
FETCH AND ADDRESS GENERATION
FETCH AND ADDRESS GENERATION
OUTPUT BRAM

## Slide 6
SYNTHESIZED DESIGN

## Slide 7
FIRST SUBMODULE : ADDER TREE

## Slide 8
FIRST SUBMODULE : ADDER TREE
Internal wires for each tree level
Level 0 has m values of input data width bits
Level 1 has m/2 values of input data width+1 bits
………………….
Level L has 1 value of input data width+L bits, where L = log2(m)
PIPE parameter
Has a parameter PIPE to toggle between pipelined and combinational implementation.
PIPE = 1 : flip flops between the stages, increases latency, shortens combinational logic path, higher clock frequency.
PIPE = 0 : result in a single clock cycle, 0 clock cycle latency, long critical path, slower clock frequency.
Intermediate results stored in flat array per level

## Slide 9
SECOND SUBMODULE : AXI READ MASTER

## Slide 10
SECOND SUBMODULE : AXI READ MASTER
Operation Overview
•Accepts a read request
•Issues AXI4 AR channel transactions
•Collects R channel data
•Result through output interface
•Handles one burst at a time
Design Overview
  3 interfaces
1. Internal request interface
2. AXI read address channel
3. AXI read data channel
  FSM contains 3 states
1. Idle state
Master waits to work
Both AXI channels inactive
2. Address read state
Holds address
Holds control signals
3. Data read state
Data words flow through FSM to
response interface

## Slide 11
THIRD SUBMODULE : WIDE-WORD BRAM

## Slide 12
THIRD SUBMODULE : WIDE-WORD BRAM
Operation Overview
•Stores one tile per address.
•Allows reading/writing 1xm tile in 1 cycle
Design Overview
  Write enable=1
Data written in specified address
  Read enable=1
Data read from specified address
  Synthesis directive
* ram_style = "block" * used for
in- built bram utilization

## Slide 13
STAGE 1 : FETCH AND ADDRESS GENERATION

## Slide 14
FETCH AND ADDRESS GENERATION FSM
Idle
Preset signals for first input request
Request input tile
  Axi request valid is set to 1
  If axi request ready=1 then axi request valid is reset
  If axi response is valid then axi response data is stored in input tile buffer till axi response last is set.
Request input tile wait
  Axi request valid is set to 1
  If axi request is ready then reset axi request valid
Request up weight tile
  If axi response valid is set then axi response data is stored weight tile buffer till axi response last
Request up weight tile wait
  if up ready=1, send input tile and up projection tile from internal buffer to respective registers
  Advance counters and pre-set next request
Send up pair to up projection
Read ReLU tile
from local BRAM
Down relay
  wait 1 cycle for bram read to be complete.
Wait relu
  relu output is present in
relu tile buffer
  Axi request valid is set to 1
  If axi request is ready then reset axi request valid
Request up weight tile
  If axi response valid is set then axi response data is stored weight tile buffer till axi response last
Request down weight tile wait
  if down ready=1, send input tile and up projection tile from internal buffer to respective registers
  Advance counters and pre-set next request
Send down pair to up projection
Done
  Set done=1
  Move to Idle state

## Slide 15
STAGE 2 & 4 : UP AND DOWN PROJECTION

## Slide 16
STAGE 3 : RELU

## Slide 17
STAGE 5 : ACCUMULATION
Start
Write path: accept result tile from down projection
if input is valid and accumulator is ready

## Slide 18
TESTBENCH OUTPUT
INPUT AND OUTPUT FROM GOLDEN MODEL
INPUT AND OUTPUT FROM DIFFERENT ITERATIONS

## Slide 19
TESTBENCH OUTPUT
OUTPUT COMPARISON BETWEEN HARDWARE AND GOLDEN MODEL

## Slide 20
TIMING DIAGRAM
RESULT

## Slide 21
RESOURCE UTILIZATION

## Slide 22
THANK YOU