## Slide 1
MODIFIED PIPELINED FFN DESIGN
Fully parallel design, FPGA board efficient implementation, block diagrams and results
July 21, 2026

## Slide 2
OVERVIEW
  Introduction
  Global Architecture Overview
  Fully pipelined FFN implementation
  Resource - efficient FFN implementation
  Resource Utilization analysis
  Latency analysis
  Throughput analysis

## Slide 3
INTRODUCTION
Background
Objectives
Earlier, fully pipelined 5 stage feed forward network was implemented, but due to massive resource utilization, a resource - optimized feed forward network has been implemented for Zync - 7000 FPGA board.
  Reduce the usage of DSP slices.
  Reduce the usage of LUT slices.
  Reduce the usage of IOB.
  Create seperate implementations considering :
1. High resource utilization, low latency
2. Low resource utilization, high latency

## Slide 4
GLOBAL ARCHITECTURE OVERVIEW
Both implementations share the same five-stage pipeline structure. The mathematical operation is y = ReLU(x · W_up) · W_down, where x is 1×D, W_up is D×4D, and W_down is 4D×D. Data is processed in tiles of size M, and the pipeline operates in two phases: UP (compute x·W_up + ReLU) and DOWN (compute ReLU_out·W_down + accumulate).

## Slide 5
VALID READY HANDSHAKE DATA TRANSFER

## Slide 6
FULLY PIPELINED FFN IMPLEMENTATION
  For tile_col = 0 to 63: (64 output column tiles)
  For inner_idx = 0 to 255: (256 ReLU row tiles)
  Fetch: relu_tile[inner_idx] from BRAM + W_down_tile[inner_idx][tile_col] from AXI
  Compute: down_proj(relu_tile, W_down_tile) → partial sum
  Accumulator: write result to output BRAM at tile_col
  For tile_col = 0 to 255: (256 output column tiles)
  For inner_idx = 0 to 63: (64 input row tiles)
  Fetch: input_tile[inner_idx] + W_up_tile[inner_idx][tile_col]
  Compute: up_proj(input_tile, W_up_tile) → partial sum
  ReLU: max(0, result) → store in ReLU BRAM at tile_col
Algorithm
Up phase
Down phase

## Slide 7
FULLY PIPELINED FFN ARCHITECTURE
FULLY PIPELINED FFN IMPLEMENTATION

## Slide 8
Sub-cycles | Columns processed
0 | 0-7
1 | 8-15
2 | 16-23
3 | 24-31
  Each projection stage uses 8 parallel multiplier column instances instead of 32. This requires ceil(32/8) = 4 cycles per inner iteration.
RESOURCE-EFFICIENT FFN IMPLEMENTATION
  This implementation uses aggressive time-multiplexing, 64-bit AXI bus, and a 64-bit output serializer to reduce the resource utilization
Design Philosophy
  Instead of 512-bit parallel output lines, output is streamed as 8 beats of 64 bits each. The internal readout FSM of the accumulator is disabled and replaced by a dedicated serializer FSM.
  64-bit AXI bus reduces IOB from 1085 to 189 pins. Weight tiles that required 32 beats on 512-bit now require 256 beats on 64-bit.

## Slide 9
RESOURCE-EFFICIENT FFN IMPLEMENTATION
Algorithm
  For tile_col = 0 to 255:
  For inner_idx = 0 to 63:
  Fetch: input_tile[inner_idx] + W_up_tile[inner_idx][tile_col]
  Cycle 0: up_proj(input_tile, W_up_tile[cols 0-7])
  Cycle 1: up_proj(input_tile, W_up_tile[cols 8-15])
  Cycle 2: up_proj(input_tile, W_up_tile[cols 16-23])
  Cycle 3: up_proj(input_tile, W_up_tile[cols 24-31])
  Accumulate into all 32 accumulator entries
  ReLU: max(0, result) → store in ReLU BRAM
Up phase
Down phase
  For tile_col = 0 to 63:
  For inner_idx = 0 to 255:
  Fetch: relu_tile[inner_idx] + W_down_tile[inner_idx][tile_col]
  Cycle 0: down_proj(relu_tile, W_down_tile[cols 0-7])
  Cycle 1: down_proj(relu_tile, W_down_tile[cols 8-15])
  Cycle 2: down_proj(relu_tile, W_down_tile[cols 16-23])
  Cycle 3: down_proj(relu_tile, W_down_tile[cols 24-31])
  Accumulate into all 32 accumulator entries
  Write result to output BRAM

## Slide 10
RESOURCE-EFFICIENT FFN IMPLEMENTATION
RESOURCE-EFFICIENT FFN ARCHITECTURE

## Slide 11
  Tiles along D = D/M = 64
  Tiles along 4D = 4D/M = 256
  Number of tiles for up phase, N_up = 256 x 64 = 16384
  Number of tiles for down phase , N_down = 64 x 256 = 16384
  Total number of tiles, N_total = 16384 x 2 = 32768
  D = 2048
  M = 32
  DATA_W = 16
  AXI_ADDR_W = 32
Parameters
Derived tile count
Adder tree pipeline depth, TD = ceil (log2(M)) = 5
Timing
  Assumed clock period, T_clk = 200 MHz
  AXI address latency, T_ar = 2 cycles
  BRAM read latency, T_bram = 2 cycles
  FSM transition overhead per tile pair, T_fsm = 3 cycles
GLOBAL & IMPLEMENTATION-SPECIFIC PARAMETERS

## Slide 12
  Number of parallel columns per projection stage = NC
  Sub-cycles per iteration, NS = ⌈M/NC⌉
  AXI data width = AW
  Elements per AXI beat = EPB = (AW/DATA_W)
  Beats per output tile = BPT = (M/EPB)
  Beats for 1xM input tile = B_in = ⌈M × DATA_W / AW⌉
  Beats for MXM weight tile = B_wt = ⌈M² × DATA_W / AW⌉
Implementation specific parameters
Derived operation count
  Total multiply-accumulate operations = MACS = 2 × D × 4D = 8D² = 33,554,432
  Element-wise ReLU operations = ReLU_ops = 4D = 8192
  Output saturation clampings = Satur_ops= 2 × M × (NT4D + NTD) = 20,480
GLOBAL & IMPLEMENTATION-SPECIFIC PARAMETERS

## Slide 13
Parameters | FULLY PARALLEL | RESOURCE-EFFICIENT
Number of parallel columns, NC | 32 | 8
Number of Subcycles per inner iteration | 1 | 4
AXI data width, AW | 512 | 64
Elements / AXI beat, EPB | 32 | 4
Beats / input tile, B_in | 1 | 8
Beats / weight tile, B_wt | 32 | 256
Beats / output tile, BPT | ---- | 8
DSP | 2048 | 512
Implementation specific parameters
GLOBAL & IMPLEMENTATION-SPECIFIC PARAMETERS

## Slide 14
DSP METRIC | EXPRESSION | FULLY-PIPELINED | RESOURCE-EFFICIENT
DSP per stage | NC × M | 1024 | 256
DSP total | 2 × NC × M | 2048 | 512
Calculated
From Synthesis report
DSP METRIC | FULLY-PIPELINED | RESOURCE-EFFICIENT
DSP usage | 900 ** | 512
DSP total | 2048 | 512
** Rest of the DSPs are mapped to LUT slices.
NC : Number of parallel columns in each projection stage
M : Tile size
RESOURCE UTILIZATION

## Slide 15
RESOURCE UTILIZATION
Fully parallel version
Resource efficient version
From synthesis reports

## Slide 16
IOB COMPONENT | EXPRESSION | FULLY-PIPELINED | RESOURCE-EFFICIENT
Input signals | clk + rst+ start + arready + rdata + rlast + rvalid | 518 | 70
Output signals | done + araddr + arlen + arsize + arburst + arvalid + rready + output_tile_data + output_tile_addr + output_tile_valid | 625 | 154
Total | Input signals + Output signals | 1143 | 224
Calculated
From Synthesis report
RESOURCE UTILIZATION

## Slide 17
RESOURCE UTILIZATION
From synthesis reports
Fully parallel version
Resource efficient version
Slice logic

## Slide 18
RESOURCE UTILIZATION
From synthesis reports
Fully parallel version
Resource efficient version
Memory

## Slide 19
T_fetch_up : Time taken in Up phase per tile pair
T_fetch_down : Time taken in Down phase per tile pair
T_proj : Time-multiplexed projection: NS sub-cycles, each with FEED→PIPE→ACC
T_up, T_down : Phase latencies
LATENCY

## Slide 20
Latency Analysis
Metric | Expression | FULLY PARALLEL | RESOURCE-EFFICIENT
T_fetch_up | T_ar + B_in + T_ar + B_wt + T_fsm = 2 + ⌈M×DW/AW⌉ + 2 + ⌈M²×DW/AW⌉ + 3 | 40 | 271
T_fetch_down | T_bram + T_ar + B_wt + T_fsm = 2 + 2 + ⌈M²×DW/AW⌉ + 3 | 39 | 263
T_proj (not last) | T_idle + NS × (T_feed + T_pipe + T_acc) = 1 + NS × (1 + TD + 1) = 1 + NS × (TD + 2) = 1 + 7·NS | 8 | 29
T_proj (last) | 1 + NS × (TD + 2) + T_out = 2 + 7·NS | 9 | 30
T_tile_up | max(T_fetch_up, T_proj) | 40 | 271
T_tile_down | max(T_fetch_down, T_proj) | 39 | 263
T_readout | NTD × (T_issue + T_relay + T_capture) = NTD × 3 = 3 × NTD or NTD × (T_wait + T_capture + BPT) = NTD × (1 + 1 + BPT) = NTD × (2 + BPT) | 192 | 640
T_up | N_up × T_tile_up + NT4D | 655,616 | 4,440,640
T_down | N_down × T_tile_down + NTD | 639,040 | 4,305,216
T_total | T_up + T_down + T_readout | 1,294,848 | 8,746,496

## Slide 21
Component | FULLY-PIPELINED | RESOURCE-EFFICIENT | % | %
AXI data transfer | 1,064,960 | 8,519,680 | 82.2% | 97.4%
AXI address phase ovehead | 98,304 | 98,304 | 7.6% | 1.1%
FSM + BRAM relay overhead | 114,688 | 114,688 | 8.9% | 1.3%
Readout | 16,896 | 13,824 | 1.3% | 0.2%
LATENCY

## Slide 22
CALCULATED THROUGHPUT
Parameter | EXPRESSION | FULLY-PIPELINED | RESOURCE-EFFICIENT
MAC throughput | MACs/T_total | 25.9 | 3.83
DSP efficiency | MACs / (T_total × DSP_count) x 100 % | 1.26% | 0.75%
BW efficiency | (Bytes_total / T_total)/(AW / 8 ) x 100 % | 82.2% | 97.4%

## Slide 23
THANK YOU!
For your attention