## Slide 1: FLASHATTENTION: Fast and Memory-Efficient Exact Attention with IO-Awareness

## Slide 2: Introduction
The time and memory complexity of self-attention are quadratic in sequence length.
Solution : FLASHATTENTION : computes exact attention with far fewer memory accesses.
Goal : 1. Compute Softmax operation without accessing whole i/p.
Solution : Tiling : Incrementally performing softmax in several passes by splitting the i/p into different blocks.
2. Not storing intermediate attention matrix for backward pass.
Solution : Store Softmax normalization factor to recompute softmax in backward pass.

## Slide 3: Algorithm

## Slide 4: Advantages of FLASHATTENTION
1. More FLOP count.
2. Far fewer memory accesses than self attention.
3. Faster in wall-clock time.
Divide matrices into tiles
Computation on each tile separately
Error introduced
Additional computation to compensate error
Main Idea

## Slide 5: FARE : A Fine-grained Pipelined Reconfigurable FlashAttention Kernel

## Slide 6: Introduction
FlashAttention lacks reconfigurability.
Due to hardware limitations, different stages of attention mechanism cannot be executed in parallel for different inputs by pipelining.
FARE allows us to do that.

## Slide 7: Overview of FARE for FlashAttention Execution and related Equations

## Slide 8
Q Matrix of dimension N X d is divided into Tr number of blocks, each with dimension Br X d
K matrix of dimension N X d is divided into Tc blocks each with dimension Bc X d
Systolic Array
Transpose
Sij
RowMax
RowSub
RowExp
RowSum
Dim : Br X Bc
Dim : Br X1
Dim : Br X Bc
Dim : Br X Bc
Dim : Br X 1
Qi
Br
d
Kj^T
d
Bc
Br
Bc
Br
Br
Bc
Br
Bc
Br
Output of STAGE 1
STAGE 1 OVERVIEW

## Slide 9: Proposed Additional Block in STAGE 1
A Prefetch Engine is a dedicated hardware control block designed to completely decouple off – chip memory latency from execution. It ensures that the systolic array in stage 1 is strictly compute – bound, not memory-bound.
The Prefetch Engine runs parallel to the main accelerator control path as an autonomous microcontroller)

## Slide 10: Basic Block Diagram of Predictive Prefetch Engine
Prefetch Engine
clk
rst
axi_arready
AXI Master Burst Memory Interface (Handshake Signals)
Host Control Interface
Engine Busy
Q base Address
Start
K base Address
axi_rdata
axi_rvalid
axi_rlast
axi_araddr
axi_arlen
axi_arvalid
axi_rready
Compute_tile_done
Prefetch_tile_ready
Current_bank
Compute Handshake Line
bram_wr_en_Q
bram_wr_addr_Q
bram_wr_data_Q
bram_wr_en_K
bram_wr_addr_K
bram_wr_data_K
BRAM Buffer Interface

## Slide 11
IDLE STATE
ADDRESS CALC STATE
AXI BURST Q STATE
WAIT STATE
AXI BURST K STATE
SWAP BANKS
YES
NO
YES
NO
Start==1?
axi_rlast ==1&& axi_rvalid==1 ?
pf_K_required==1 ?
NO
YES
axi_rlast ==1&& axi_rvalid==1 ?
NO
YES
Compute_tile_done==1?
NO
YES
J_pf==T_c && i_pf==0 ?
NO
YES
FSM Design for the Prefetch Engine

## Slide 12
Look Ahead Address Generator Logic
Initialize i_pf = 0, j_pf = 0, pf_K_required = 1
Calculate Byte Offsets :
Offset_Q = B_R* D_MODEL
Offset_K = B_C* D_MODEL
Compute Physical Target addresses :
next_addr_Q = addr_Q_base + (i_pf * Offset _Q)
next_addr_K = addr_K_base + (j_pf * Offset _K)
Advance Prefetch counters for the following tile
i_pf = i_pf + 1
if i_pf == T_R:
i_pf = 0
j_pf = j_pf + 1
pf_K_required = 1
else: pf_K_required = 0

## Slide 13
Host Control Interface
Engine Busy
Q base Address
Start
K base Address
Allows the central processor to initiate, configure, monitor prefetch engine
A single cycle clock pulse sent by central processor to command engine to start execution
A multi bit bus holding the absolute physical address where Q matrix starts in HBM. It provides the starting point for Look Ahead Address Generation Unit.
A multi bit bus holding the absolute physical address where K matrix starts in HBM. It provides the starting point for fetching K tiles.
A multi bit bus holding the absolute physical address where Q matrix starts in HBM. It provides the starting point for Look Ahead Address Generation Unit.
Different Input and Output Signals for Prefetch Engine

## Slide 14
Compute_tile_done
Prefetch_tile_ready
Current_bank
Compute Handshake Line
Synchronizes Prefetch Engine with Stage 1 Systolic Array. Prevents Data Race, Overwriting, Execution Stalls
Driven by Stage 1 Compute Controller back to Prefetch Engine. It is a release signal, informing the engine that systolic array has finished executing the operations on the current tiles. The exact clock edge when compute_tile_done goes high, Prefetch Engine transitions from Wait State to Swap Banks State.
Driven by Prefetch Engine to Stage 1 Compute Controller. It is a guarantee signal assuring that the next required tiles are completely fetched from the HBM.
Pointer flag for the dual bank memory allocation. It decides which physical half of the on-chip BRAM addresses(0-2047/2048-4095) belongs to the Prefetch Engine and which half belongs to the Compute Engine. When current_bank=0, Prefetch Engine writes incoming AXI data to Bank 0 and Compute Engine reads from Bank 1. During Swap Banks State, this bit flips, and ownership inverts

## Slide 15
axi_arready
AXI Master Burst Memory Interface (Handshake Signals)
axi_rdata
axi_rvalid
axi_rlast
axi_araddr
axi_arlen
axi_arvalid
axi_rready
Manages the block data transfers between Prefetch Engine and HBM
Output Address Bus. It points the external memory controller to the memory offset of the required Q or K block.
8 bit signal tells the memory controller to send 8 bit data after getting address request from the Output Address Bus.
Address handshake pair. axi_arvalid means the requested address is stable and real, while axi_arready means that the memory controller is free and accepted the request.
Input Data Bus. Carries actual matrix from the HBM to on chip DRAM.
Data handshake pair. axi_rvalid means that a valid data is sitting on the axi_rdata bus, while axi_rready means that the Prefetch Engine is free and accepted the data.
1 bit marker flag that informs the prefetch engine that the current item on the data bus is the absolute final piece of the requested tile. The exact cycle when axi_rlast and axi_rvalid are both true, the FSM terminates burst state, resets the element tracking counters an checks if thenext matrix tile is needed to be fetched.

## Slide 16
bram_wr_en_Q
bram_wr_addr_Q
bram_wr_data_Q
bram_wr_en_K
bram_wr_addr_K
bram_wr_data_K
BRAM Buffer Interface
Directly connected to the on-chip dual port DRAM. Prefetch engine only owns the write port of it.
1 bit control signals that tell BRAM exactly when to write data. bram_wr_en_Q is driven high only when the FSM is in AXI BURST Q State and axi_rvalid=1. The same applies to bram_wr_en_K.
Output Address Buses. Multi bit bus specifies the row index inside the BRAM where the incoming data must be written.
For Q : if current_bank=0, then bram_wr_addr_Q = element_count, if current_bank=1, then bram_wr_addr_Q = element_count + 2048
For K : Instead of linear index, it drives transposition calculation:
address = k_col_count * B_C + k_row_count.
Pass the raw matrix element values received from the off-chip HBM to BRAM. These buses are directly registered to axi_rdata bus.

## Slide 17
IDLE STATE
i_pf<-0, j_pf<-0
engine_busy <-0
prefetch_tile_ready<-0
pf_K_required<-1
current_bank<-0
ADDRESS CALC STATE
engine_busy <-1
prefetch_tile_ready<-0
axi_araddr <-addr_Q_base + (i_pf*offset_q)
axi_arlen<-(B_R*D_MODEL)-1
axi_arvalid<-1
i_pf<-i_pf +1
If i_pf +1==T_R
i_pf<-0
j_pf<-j_pf +1
pf_K_required<-1
Else pf_K_required<-0
AXI BURST Q STATE
If axi_arvalid ==1&& axi_arready==1
axi_arvalid<-0
If axi_rlast ==1&& axi_rvalid ==1&& pf_K_required==1
axi_araddr<-addr_K_base + (j_pf*offset_k)
axi_ arlen<-(B_C*D_MODEL)-1
axi_arvalid<-1
AXI BURST K STATE
If axi_arvalid==1 && axi_arready==1
axi_arvalid<-0
WAIT STATE
prefetch_tile_ready<-1
SWAP BANKS STATE
prefetch_tile_ready<-0
current_bank<-~current_bank
Value of Different Control Signals at Different States

## Slide 18: Memory Streaming and Matrix Transpose Logic
Default write strobes down
bram_wr_en_Q <-0, bram_wr_en_K <-0;
If (current_state==AXI BURST STATE && axi_rvalid==1)
bram_wr_en_Q <-1, bram_wr_data_Q<-axi_rdata
bram_wr_addr_Q <= (current_bank == 1'b0) ? element_count : (element_count + 2048);
if (axi_rlast==1) then element_count<-0
else element_count<-element_count+1

## Slide 19
If (current_state==AXI BURST STATE K && axi_rvalid==1) then
bram_wr_en_K<-1, bram_wr_data_K<-axi_data;
bram_wr_addr_K<-(current_bank==0)?(K_col_count*B_C*K_row_count):(K_col_count*B_C+K_row_count + 2048)
If (K_col_count==D_MODEL-1) then k_col_count<-0
{
If (K_row_count==B_C-1) then K_row_count<-0
Else K_row_count <- K_row_count +1
}
Else K_col_count <- K_col_count +1

## Slide 20: Advantages of Prefetch Engine
1. Overlaps off-chip memory access with systolic array execution. The next data tile is already loaded before the current computation loop ends.
2. Eliminates execution stalls in systolic array processing elements.
3. Executes K matrix transposition on-the-fly inside BRAM routing wires.
4. Fetches stationary K tiles only when the inner loop overflows.

## Slide 21
Thank You