## Slide 1: Faster Matrix Multiplication In Feed Forward Network Using Tiling and Tensor Core and Design of Pipelined Feed Forward Network

## Slide 2: Introduction
1. we want to project a row vector input across all column vectors of up projection matrix simultaneously
3. we need fully parallel Vector Matrix Multiplier
2. We have to broadcast the input vector to multiple processing elements at the exact same time
4. Instead of having one neuron cycle through the data, we will duplicate our dot product logic for every single column in our matrix
5. While the approach gives us absolute lowest latency possible (1 projections per cycle), it scales quadratically in terms of hardware resources and we will run out of dsp blocks.
6. If our matrix is too large to do multiplication completely simultaneously, we modify this to be semi-parallel (process some number of coloumns simultaneously, cycle through the rest using FSM, and store the weights in BRAM blocks).

## Slide 3
1 x d vector
d x 4d up projection matrix
Taking 4 columns at a time
d multipliers
+ (d-1) adders
Number of Tiles = (4d/4) = d
Total Resource Utilization = (d x (d + d – 1)) = d(2d – 1)
Latency = (1 + log(d)) x 4
Throughput = 4d/4 = d
Explaining Tiling with Tensor Core with an Example

## Slide 4
1 x d vector
d x 4d up projection matrix
Taking m columns at a time
d multipliers
+ (d-1) adders
Number of Tiles = (nd/m)
Total Resource Utilization = ((nd/m) x (d + d – 1)) = (nd/m) (2d – 1)
….
….
….
Projection Matrix Dimension = n
Latency = (1 + log(d)) x m
Throughput = (nd/m)
Explaining Tiling with Tensor Core (Generalized)

## Slide 5: Design Choices Used
size of the input row vector is 1x8
the size of up projection matrix is 8x32
up projection matrix is partitioned into 4 tiles, each of size 8x8
size of the down projection matrix is 32x8
for valid matrix multiplication, the down projection matrix is transposed
partitioned into 4 tiles of 8x8 size
up and down projection matrix tiles are fetched from BRAM
BRAM is dynamically loaded with weight tiles from an external memory

## Slide 6: Algorithmic Representation of Pipelined Feed Forward Network
Multiply 1x8 input vector with 8 x 8 up projection matrix corresponding to tile_index
Start
Initialize tile_index = 0, 8-register accumulator bank to 0
Pass the previous cycle’s up projection output through ReLU
Multiply the previous cycle’s ReLU output with 8x8 transposed down projection matrix tile corresponding to tile_index, and add it element-wise directly into the 8 register bank.
Increment tile_index by 1
Tile_index == 4 ?
Stop
yes
no

## Slide 7: Basic Representation of Pipelined Feed Forward Network
Pipelined FFN
clk
rst
start
Row vector input
BRAM up projection data bus
BRAM down projection data bus
BRAM up projection address bus
BRAM down projection address bus
done
Accumulator register bank
[8 x 16 -1 : 0 ]
[8 x 16 -1 : 0 ]
[1 : 0 ]
[1 : 0 ]
[15 : 0 ]
[15 : 0 ]

## Slide 8: FSM Control Path Diagram
cycle_count= 0
running = 0
Start = 0
IDLE
ACTIVE
Initialization state
cycle_count= 6
running = 1
done = 1
Start = 1
running = 0
cycle_count += 1

## Slide 9: The Requirement of 6 cycles
The 4-Stage Data Pipeline (4 Cycles)
Stage 1 (_s1): Input latching and initial matrix processing setup.
Stage 2 (_s2): up-projection matrix multiplication
Stage 3 (_s3): Application of the rectified linear activation function
Stage 4 (_s4): down-projection matrix multiplication.
Pipeline Overhead & FSM Control (2 Cycles)
Ingress Cycle (Latch/Setup): 1 cycle is required at the beginning to transition the FSM from an idle state to active (running = 1), sampling the valid input vector and asserting the first validity qualifier (valid_s1).
Egress Cycle (Writeback & Done): 1 cycle is needed at the end of the pipeline to accumulate the final down-projection results into the accumulator_bank and safely assert the done control signal to notify external blocks that the output is stable.

## Slide 10: The Pipelined Architecture Timeline
Clock Cycle | running State | main_counter Value | Hardware Operation
Idle | 0 | 0 | System is waiting for a start pulse.
Cycle 0 | 1 (Active) | 0 | start received. Addresses Tile 0 from BRAM.
Cycle 1 | 1 (Active) | 1 | Addresses Tile 1 from BRAM.
Cycle 2 | 1 (Active) | 2 | Addresses Tile 2 from BRAM.
Cycle 3 | 1 (Active) | 3 | Addresses Tile 3 (Final Tile) from BRAM.
Cycle 4 | 1 (Active) | 4 | Stops addressing BRAM. Up-Projection finishes processing Tile 3.
Cycle 5 | 1 (Active) | 5 | Down-Projection finishes processing Tile 2.
Cycle 6 | 1  0 | 6 | Down-Projection finishes processing Tile 3. done fires; system turns off.

## Slide 11: Block Diagram Representation of Feed Forward Network
Stage 1 : Address Generation
Stage 2 : Up Projection
Stage 3 : ReLU Activation
Stage 4 : Down Projection
valid_s1
valid_s2
valid_s3
valid_s4
done
tile_idx_s1
tile_idx_s2
tile_idx_s3
tile_idx_s4
clk
rst
up_proj_out
relu_out
accumulator_bank
start
down_bram_addr
down_bram_rdata
up_bram_addr
up_bram_rdata
row_input_latch
row_input
row_in_elements
Cycle_count
running
up_mult
up_acc
down_mult
down_acc

## Slide 12: Stage 1 : FSM controller and Address Generation
rst = 1
cycle_count <= 0;
running <= 1'b0;
valid_s1 <= 1'b0;
tile_idx_s1 <= 0;
up_bram_addr <= 0;
row_input_latch <= 0;
YES
NO
start ==1
YES
running <= 1’b1;
cycle_count <= 0;
valid_s1 <= 1'b1;
tile_idx_s1 <= 0;
up_bram_addr <= 0;
row_input_latch <= row_input;
running==1
cycle_count < 3
cycle_count <= cycle_count + 1;
tile_idx_s1 <= tile_idx_s1 + 1;
up_bram_addr <= tile_idx_s1 + 1;
valid_s1 <= 1'b1;
NO
valid_s1 <= 1'b0;
YES
NO
cycle_count=6
running <= 1'b0;
cycle_count <= cycle_count + 1;
IDLE STATE
&&rst = 0
ACTIVE STATE
valid_s1 <= 1'b0;
YES
NO

## Slide 13: CONTROL PATH PROPAGATION
rst = 0
YES
valid_s2 <= 0;
tile_idx_s2 <= 0;
valid_s3 <= 0;
tile_idx_s3 <= 0;
valid_s4 <= 0;
tile_idx_s4 <= 0;
done <= 0;
NO
valid_s2 <= valid_s1;
tile_idx_s2 <= tile_idx_s1;
valid_s3 <= valid_s2;
tile_idx_s3 <= tile_idx_s2;
valid_s4 <= valid_s3;
tile_idx_s4 <= tile_idx_s3;
done <= valid_s4 && (tile_idx_s4 == 2'b11);
Start
Stop

## Slide 14: STAGE 2: Up-Projection
rst = 0
up_proj_out <= 0;
valid_s2 = 1
YES
NO
initialize i=0;
up_acc = 0;
initialize j=0;
up_mult = row_in_elements[j] * up_w_matrix[i][j];
up_acc = up_acc + (up_mult >>> FRAC_BIT);
j < N
j=j+1;
up_proj_out[i*BIT_WIDTH +: BIT_WIDTH] <= up_acc;
i < N
Start
Stop
YES
NO
YES
NO
i=i+1;

## Slide 15: STAGE 3: ReLU Activation Function
Start
rst = 0
relu_out <= 0;
YES
NO
valid_s3 = 1
YES
initialize k=0;
relu_out[k*BIT_WIDTH +: BIT_WIDTH] <= {BIT_WIDTH{1'b0}};
k=k+1;
YES
up_proj_elements[k][BIT_WIDTH - 1] == 1'b1
relu_out[k*BIT_WIDTH +: BIT_WIDTH] <= up_proj_elements[k];
remain in stage 2
NO
NO
k<n
down_bram_addr = tile_idx_s3;
stop
YES
NO

## Slide 16: STAGE 4: Down Projection & Accumulation Bank
Start
rst = 0
accumulator_bank <= 0;
NO
YES
NO
start=0
accumulator_bank <= 0;
YES
valid_s4=1
initialize x=0;
down_acc = 0;
initialize y=0;
down_mult = relu_elements[y] * down_w_matrix[x][y];
down_acc = down_acc + (down_mult >>> FRAC_BIT);
y = y+1;
y<n
accumulator_bank[x*BIT_WIDTH +: BIT_WIDTH] <=
accumulator_bank[x*BIT_WIDTH +: BIT_WIDTH] + down_acc;
x = x+1;
x<n
Stop
NO
YES
remain in stage 3

## Slide 17: Hardware Performance Parameters
Execution Time = tdone – tstart
tdone = 60000 ps, tstart = 211000 ps
Execution Time = (211000 – 60000) ps = 151000 ps = 151 ns.
Clock Cycle Latency = Number of Clock edges pass between the time data enters a circuit and the time the corresponding result exits.
Absolute latency = Clock cycles x Tclk
Tclk = 20 ns
Clock cycles = 4
Absolute latency = 20 x 4 = 80 ns

## Slide 18: Hardware Performance Parameters
Clock frequency, fclk = (1/20) MHz = 50 MHz
Throughput :
1. Data throughput = (2x8x8x16)bits/cycle x fclk
= 102.4 Gbps
Operations throughput = 128 MACs/cycle x fclk
= 6.4 GMACs/s
= 256 operations/cycle x fclk
= 12.8 GOPS

## Slide 19: Hardware Performance Parameters
Resource Utilization :

## Slide 20: Limitation
Further Advancement Needed
Modelling BRAM to store up and down projection matrix tiles
Modelling the AXI interface from external memory and internal BRAM for dynamic tile fetching.
Bonded IOB utilization overflowed.

## Slide 21: Thank You